## Slide 1: Implementing new domains in SPECFEM++
Rohit Kakodkar
Research Software Engineer II
PICSciE / Geosciences

## Slide 2: SPECFEM Algorithm
Start
Define parameter file
Define sources
Define receivers
Read the mesh
Generate assembly
Define global numbering scheme.
Define GLL level properties
Run solver
Execute the time loop
Write output
for (int istep : nstep) {
apply_predictor_phase_forward();
compute_source_interaction();
compute_forces();
divide_by_mass_matrix();
apply_corrector_phase_forward();
}
Time loop

## Slide 3: SPECFEM++ Architecture
Acoustic
Elastic
Isotropic
Dirichlet
Stacey
None
void compute_forces() {
compute_forces_elastic_isotropic_none();
compute_forces_acoustic_isotropic_none();
compute_forces_elastic_isotropic_stacey();
compute_forces_acoustic_isotropic_dirichlet();
.
.
.
}
*This is a representative code

## Slide 4: Outline
Preparation
Read the mesh
Bookkeeping
Physics implementation
Post-processing

## Slide 5: Preparation
Define enumerations
Define properties
Define misfit kernels

## Slide 6: Preparation
Define enumerations
Define properties
Define misfit kernels
medium.hpp
material_definitions.hpp

## Slide 7: Preparation
Define enumerations
Define properties
Define misfit kernels
medium.hpp
material_definitions.hpp
enum class medium_tag {
elastic,
acoustic
};
template <>
class attributes<dim2, elastic> {
public:
constexpr static int dimension() { return 2; }
// Number of components in field constexpr static int components() { return 2; }
};

## Slide 8: Preparation
Define enumerations
Define properties
Define misfit kernels
medium.hpp
material_definitions.hpp
#define ELEMENT_TYPES\
((DIM2, ELASTIC, ISOTROPIC, NONE))( \
(DIM2, ACOUSTIC, ISOTROPIC, NONE))( \
(DIM2, ELASTIC, ISOTROPIC, STACEY))( \
(DIM2, ACOUSTIC, ISOTROPIC, DIRICHLET))
void compute_forces() {
compute_forces_elastic_isotropic_none();
compute_forces_acoustic_isotropic_none();
compute_forces_elastic_isotropic_stacey();
compute_forces_acoustic_isotropic_dirichlet();
.
.
.
}

## Slide 9: Preparation
Define enumerations
Define properties
Define misfit kernels
medium.hpp
material_definitions.hpp
#define ELEMENT_TYPES\
((DIM2, ELASTIC, ISOTROPIC, NONE))( \
(DIM2, ACOUSTIC, ISOTROPIC, NONE))( \
(DIM2, ELASTIC, ISOTROPIC, STACEY))( \
(DIM2, ACOUSTIC, ISOTROPIC, DIRICHLET))
void compute_forces() {
#define COMPUTE_FORCES(DIMENSION, MEDIUM, PROPERTY, BOUNDARY) \
compute_forces<DIMENTION, MEDIUM, PROPERTY, BOUNDARY>();
CALL_MACRO_FOR_ALL_ELEMENT_TYPES(COMPUTE_FORCES,
WHERE(DIM2)
WHERE(ACOUSTIC, ELASTIC)
WHERE(ISOTROPIC) WHERE(NONE, STACEY, DIRICHLET));
}

## Slide 10: Preparation
Define enumerations
Define properties
Define misfit kernels
7 lines
3 - 10 lines
3 - 10 lines

## Slide 11: Read the mesh
Update the mesh reader
80 lines
Reads the MESHFEM2D mesh binary file line-by-line

## Slide 12: Bookkeeping
Define element types
Update data containers
Add new sources
Add new receivers
Define properties
Define misfit kernels
Add wavefields

## Slide 13: Bookkeeping
Define element types
Update data containers
Add new sources
Add new receivers
Define properties
Define misfit kernels
Add wavefields
CALL_MACRO_FOR_ALL_ELEMENT_TYPES(UPDATE_CONTAINER,
WHERE(DIM2)
WHERE(ACOUSTIC, ELASTIC)
WHERE(ISOTROPIC, ANISOTROPIC)
WHERE(NONE, STACEY, DIRICHLET, COMPOSITE));

## Slide 14: Bookkeeping
Define element types
Update data containers
Add new sources
Add new receivers
Define properties
Define misfit kernels
Add wavefields
CALL_MACRO_FOR_ALL_ELEMENT_TYPES(UPDATE_CONTAINER,
WHERE(DIM2)
WHERE(ACOUSTIC, ELASTIC, POROELASTIC)
WHERE(ISOTROPIC, ANISOTROPIC)
WHERE(NONE, STACEY, DIRICHLET, COMPOSITE));

## Slide 15: Bookkeeping
Define element types
Update data containers
Add new sources
Add new receivers
Define properties
Define misfit kernels
Add wavefields
4 lines†
21 lines†
14 lines†
6 lines†
10 – 20 lines
10 – 20 lines
7 lines†

## Slide 16: Physics Implementation
void compute_forces() {
for (int ispec : nspec){
for (int iz : ngllz){
for (int ix : ngllx){
s_grad = compute_gradients(s);
stress = compute_stress(s_grad);
sigma = compute_integrand(stress);
acceleration = divergence(sigma);
update_acceleration(acceleration);
}
}
}
}

## Slide 17: Physics Implementation
Compute mass matrix
Compute stress
Compute source interaction
Compute seismograms
Update the timescheme
specfem::datatype::VectorPointViewType<type_real, 2, 1, UseSIMD> T;
T(0, 0) = properties.rho_inverse * du(0, 0);
T(1, 0) = properties.rho_inverse * du(1, 0);
return { T };
Acoustic stress
datatype sigma_xx, sigma_zz, sigma_xz;
sigma_xx = properties.lambdaplus2mu * du(0, 0) + properties.lambda * du(1, 1);
sigma_zz = properties.lambdaplus2mu * du(1, 1) + properties.lambda * du(0, 0);
sigma_xz = properties.mu * (du(0, 1) + du(1, 0));
specfem::datatype::VectorPointViewType<type_real, 2, 2, UseSIMD> T;
T(0, 0) = sigma_xx;
T(0, 1) = sigma_xz;
T(1, 0) = sigma_xz;
T(1, 1) = sigma_zz;
Elastic stress

## Slide 18: Post processing
Write properties
Write misfit kernels
Write seismograms

## Slide 19: Summary
Preparation
Read the mesh
Bookkeeping
Physics implementation
Post-processing
400 lines
Electromagnetic implementation compute forces : ~300 lines

## Slide 20: Damping
void compute_forces() {
for (int ispec : nspec){
for (int iz : ngllz){
for (int ix : ngllx){
s_grad = compute_gradients(s);
stress = compute_stress(s_grad);
sigma = compute_integrand(stress);
acceleration = divergence(sigma);
apply_damping(velocity, acceleration);
update_acceleration(acceleration);
}
}
}
}